# EBOX-IMX8MM UART Overview

The there are 4x UART on EBOX-IMX8MM, and the default settings of them are:

UART1 is connected to the WLAN/Bluetooth module

# UART 2 is connected to the console function

UART 3 is connected to the J19 connector on the board.

UART 4 is connected to the J21 connector on the board.

If it is a no WLAN/Bluetooth Module version, the UART1 will be connected to the J15 connector on the board.

# UART naming under Linux

UART 1: /dev/ttymxc0

# UART 2: /dev/ttymxc1

UART 3: /dev/ttymxc2

UART 4: /dev/ttymxc3

Download the testing tool in the link below and put it in the root file of the Linux

ftp://sbc:sbc@ftp.icop.com.tw/iMX8/OS/Yocto/Testing/UART/linux-serial-test.dat

Testing UART3：

# ./linux-serial-test -p /dev/ttymxc2 -o 5 -i 6 -c

Testing UART4：

#  ./linux-serial-test -p /dev/ttymxc3 -o 5 -i 6 -c